## Slide 1
Adding, Subtracting, Multiplying, and Dividing

## Slide 2
int myValue;
myValue = 1 + 2; // addition
myValue = 3 - 2; // subtraction
myValue = 3 * 2; // multiplication
myValue = 3 / 2; // division (the result is 1)
Make sure your result will not exceed the maximum size of the destination variable.

## Slide 3
int value = 1 + 2 * 3 + 4;
int value = 1 + (2 * 3) + 4;
int value = ((1 + 2) * 3) + 4;

## Slide 4: Incrementing and Decrementing Values
int myValue = 0;
myValue = myvalue + 1; // this adds one to the variable
myValue myValue += 1; // this does the same as the above
myValue = myvalue - 1; // this subtracts one from the variable myValue myValue -= 1; // this does the same as the above
myValue = myvalue + 5; // this adds five to the variable
myValue myValue += 5; // this does the same as the above
myValue += 1; // this does the same as the above

## Slide 5: Finding the Remainder After Dividing Two Values
Use the % symbol (the modulus operator) to get the remainder:
int myValue0 = 20 % 10; // get the modulus(remainder) of 20 divided by 10 int
myValue1 = 21 % 10; // get the modulus(remainder) of 21 divided by 10 myValue0 equals 0 (20 divided by 10 has a remainder of 0). myValue1 equals 1 (21 divided by 10 has a remainder of 1).
using 2 with the modulus operator, the result can be used to check if a value is odd or even:
int myValue; //... code here to set the value of myValue
if (myValue % 2 == 0) {
Serial.println("The value is even");
}
else { Serial.println("The value is odd");

## Slide 6: Determining the Absolute Value
abs(x) computes the absolute value of x. The following example takes the absolute value of the difference between readings on two analog input ports (see Chapter 5 for more on analogRead()):
int x = analogRead(0);
int y = analogRead(1);
if (abs(x-y) > 10) { Serial.println("The analog values differ by more than 10"); }
abs(x-y); returns the absolute value of the difference between x and y. It is used for integer (and long integer) values.

## Slide 7: Constraining a Number to a Range of Values
constrain(x, min, max) returns a value that is within the bounds of min and max:
myConstrainedValue = constrain(myValue, 100, 200);
myValue (the input value)
constrain(myValue, 100, 200)
99 100
100 100
150 150
200 200
201 200

## Slide 8: Finding the Minimum or Maximum of Some Values
min(x,y) returns the smaller of two numbers. max(x,y) returns the larger of two numbers:
myValue = analogRead(0);
myMinValue = min(myValue, 200); // myMinValue will be the smaller of myVal or 200
myMaxValue = max(myValue, 100); // myMaxValue will be the larger of myVal or 100

## Slide 9: Raising a Number to a Power
pow(x, y) returns the value of x raised to the power of y:
myValue = pow(3,2); This calculates 3^2 , so myValue will equal 9.

## Slide 10: Generating Random Numbers
Use the random function to return a random number. Calling random with a single parameter sets the upper bound;
the values returned will range from zero to one less than the upper bound: random(max); // returns a random number between 0 and max -1 Calling random with two parameters sets the lower and upper bounds;
the values returned will range from the lower bound (inclusive) to one less than the upper bound:
random(min, max); // returns a random number between min and max -1